## Slide 1: August 8, 2019
Take out some paper for note-taking.
“Have you ever taken a photo of a friend and it came out badly?”

## Slide 2: Camera Basics
Using a Camera

## Slide 3: Types of Cameras
Still Cameras
  Fixed Lens Cameras
    Lens is not interchangeable (removable)
    Variable zoom, controlled by servo controller
    User friendly, less manual
    features
    Less expensive (<$500)

## Slide 4: Types of Cameras
Still Cameras
  Single Lens Reflex (SLR)/Digital SLR
    Lens is interchangeable (removable)
    Professional quality, more manual features
    More expensive ($500+)
    Lenses often sold separately

## Slide 5: Types of Cameras
Video Cameras
  Studio Camera
    Designed for studio use only
      Very expensive ($50,000+)
      Very high quality
      Not used to record audio
      No built-in recorder
      Camera Control Unit separate
        Color balance, iris and other controls not adjusted on camera
      Heavy and difficult to transport
        Requires a pedestal mount

## Slide 6: Types of Cameras
Video Cameras
  Camcorder
    Used for field production (outside studio)
      Portable and durable
      Records to tape, card, or built-in hard drive
      Records audio
        Built-in microphone
        High quality audio inputs
      Various types of camcorders
        Professional (ENG) – ($10,000+)
        Consumer – ($300+)
        Prosumer – ($3000-10,000)

## Slide 7: Types of Cameras
HDSLR Cameras
  Growing popularity of using DSLR cameras for shooting HD video
    Lens is interchangeable (removable)
      Lenses give more cinematic look
    Cameras often shoot multiple frame rates
    Requires more accessories
    for quality video capture
      Audio capture (microphone)
      Mounting device (video rig)
      Follow focus
      External video screen

## Slide 8: August 9, 2019
Take out some paper for note-taking.
Warm up:
Name the types of cameras we discussed yesterday. Give an example of each.

## Slide 9: Resolution
Digital images are made up of pixels
  The more pixels, the higher quality the image
  Higher resolution images take up more digital space on the storage device (memory card, videotape, hard drive, etc.)
  Measured in pixel columns by pixel rows
    640x480 – analog standard definition video
    1920x1080 – high definition (HD) video
    2048x1536 – 3,145,728 pixels (3.1 megapixels)
  DPI – dots per inch
    Measures the density of dots per inch in a digital print
    The higher the dpi, the better quality the print
      Examples: 72, 96, 150, 300 dpi
      Images for print should be created at 300 dpi, text at 400 dpi

## Slide 10: Resolution
72 dpi
300 dpi

## Slide 11: Camera Controls
Cameras have a number of different functions.
Some settings are found only on still cameras, some on video cameras or some on both
The following controls may be automatically or manually adjusted
  Manual means the operator adjusts the camera
  Automatic means the camera selects the best setting for the given conditions.

## Slide 12: Camera Controls
White balance (still and video cameras)
  Gives the camera a “true white”, adjusting all other colors accordingly.
  As lighting changes from one location to another, WB should be adjusted
  May have multiple modes for white balance
    Auto WB
    Indoor WB
    Outdoor WB
    Manual (custom) WB
      When in manual mode the symbol often blinks when it needs setting and is solid when WB is set
      Manually set WB by zooming in or focusing on a white surface
“white balance” icons on
many still cameras

## Slide 13: White Balance
The picture (right) shows an outdoor scene with indoor white balance settings. (Note the blue tint)
The picture (left) shows an outdoor scene with proper outdoor white balance settings.

## Slide 14: Camera Controls
ISO aka “Film Speed” (still cameras)
  Determines how sensitive the camera’s image sensor is to light
    The lower the ISO, the slower the speed
      Lower ISO when possible
      High ISO results in more grainy photos
      Common ISOs are 100, 200, 400 and 800
    ISO setting recommendations
      100-200: outdoors, sunny conditions
      400-800: outdoors, cloudy conditions
      1600: night time, low light

## Slide 15: Camera Controls
Iris (still and video cameras)
  The iris controls the amount of light entering into the lens
  The lower the light conditions, the wider the aperture (opening) should be
  Iris is measured in f-stops
    f/1.4, f/2, f/2.8
    As f-stop numbers get larger, the aperture gets smaller (and vice-versa)

## Slide 16: Iris
The picture (right) shows an outdoor scene with an improper iris setting.
The picture (left) shows an outdoor scene with a proper iris setting.

## Slide 17: Camera Controls
Shutter speed (still and video cameras)
  Allows for shooting of fast moving objects without blurring
  The faster the subject, the faster the speed
  Measured in fractions of a second
    1/60 (of a second) – slow shutter
    1/2,000 - fast shutter
  The faster the shutter speed, the less light the camera lens allows in

## Slide 18: August 12, 2019
Warm-up:
Why is it important to ‘white balance’?
What is the purpose of the iris?

## Slide 19: Shutter Speed
The difference between these two photographs is shutter speed. The bottom photo shows a faster shutter speed than the top. The pinwheel (which is moving) is clear and seems to be frozen in mid-air.

## Slide 20: Camera Controls
Gain (video cameras)
  Boosts the video signal in low light conditions.
  Gain affects resolution.
    Gain creates “video noise”
    The higher the gain, the lower the resolution.
  Gain is measured in decibels
    +6 dB, +9 dB, +12 dB

## Slide 21: Gain
The picture below shows how boosting the gain gives the appearance of more light, but adds video noise, making it look “grainy”.

## Slide 22: Camera Controls
ND Filter (Neutral Density Filter)
  Filters out bright sunlight to avoid overexposure
  May be a camera setting (video)
  May be an actual filter placed on the front of the lens (photo)

## Slide 23: Camera Controls
Focal Length
  Distance from lens to imaging sensor
  Determines the picture’s angle of view (magnification)
    As focal length increases
      Angle of view becomes more narrow
      Less elements are visible
Zoom (increase in focal length)
  May be controlled with the servo zoom control on the camera or by manipulating the lens (DSLR)
  Zoom may be measured in millimeters (photography) or “power” (video)

## Slide 24: Camera Controls
  Optical zoom – focal length changes
    No quality loss when going wide to narrow
  Digital zoom – focal length doesn’t change, the camera enlarges the image
    Pixels are enlarged
    Loss of quality
  To determine optical zoom power, divide the zoom setting by the widest setting, ie 500mm/50mm = 10x
    If a lens has a zoom range of 18mm – 270mm…
      18-35mm (1-2x ) = wide angle
      36-70mm ( 3-4x) = normal angle
      135-270mm (7-15x) = telephoto

## Slide 25: Zoom
The photos below show the difference between optical zoom (left) and digital zoom (right). Notice the pixilation on the digital zoom.
Optical Zoom (approx. 7x)
Digital Zoom
Wide Angle (no zoom)

## Slide 26: August 13, 2019
Warm-up:
What is the difference between ‘optical zoom’ and ‘digital zoom’?

## Slide 27: Camera Controls
Focus (both still and video)
  Sharpness or clarity of an image
    Manually adjusted with the focus ring located on lens
  Selective focus
    Creates variety, interest and emphasis in the shot
    Must be zoomed in (the farther, the more dramatic)
    Must have significant distance between foreground and background
  Rack focus
    Focus is shifted while recording video
In selective focus, we have a foreground subject in focus (rose) and a subject in the background (church) out of focus.

## Slide 28: Camera Controls
Focus (cont.)
  MOD – minimum object distance
    This is the point at which a lens is too close to the subject to focus
    MOD can be decreased (ie from six inches to three inches) with a macro, allowing the camera to focus at a closer distance
    Macro may be a lens attachment or a setting on the camera
“macro” icon on many
still cameras

## Slide 29: Camera Controls
This picture was taken with macro settings. Notice the contrast in focus between the foreground (close to the camera) and background.

## Slide 30: Basic Camera Care
Handle the camera with care
Do not point the lens at the sun, bright lights or bright reflections for an extended period of time
Do not clean the camera or the lens with solvents, liquids, or chemicals
  Use clean, dry cloth for camera; lens cloth for lenses
Do not touch a camera lens
  Keep covered when not in use
Do not operate or store equipment in extreme temperatures or weather